## Slide 1
Concentration Polarization of LDL
in the Arterial System
Governing Equations, Boundary Conditions & Computational Model
Fatouraee, Deng, De Champlain & Guidoin | Ann. N.Y. Acad. Sci., 1998

## Slide 2
Model Assumptions, COMSOL Parameters & Modules
Assumptions
Homogeneous, incompressible, Newtonian blood
Straight cylindrical vessel, uniform diameter
Vessel wall permeable to LDL (Vw ~ 10⁻⁶ cm/s)
Pulsatile inlet: Womersley velocity profile
Uniform inlet LDL concentration (C = C₀)
COMSOL Modules
Laminar Flow (spf) — fluid flow solver
Transport of Diluted Species (tds) — LDL mass transport
COMSOL Parameters
Name
Value
Description
R₀
0.0035 m
Internal radius of artery
L
0.035 m
Length of segment (10·R₀)
ρb
1050 kg/m³
Density of blood
μb
0.0035 Pa·s
Dynamic viscosity
D
5E-12 m²/s
Diffusion coefficient
Vw
4E-8 m/s
Filtration velocity
Q
275 ml/min
Flow rate
c₀
1 mol/m³
Inlet concentration
f
70 /min
Heart rate
T
0.857 s
Cardiac period (1/f)

## Slide 3
Geometry
Geometry
Inlet Flow Rate Profile

## Slide 4
Governing Equations
Fluid Flow Equations
(Laminar Flow)
Mass Transport Equations
(Transport of Diluted Species)
J = diffusive flux | R = reaction rate term
Navier-Stokes Equation
Continuity Equation
Convection-Diffusion
Equation
Fick’s Diffusion Law
p = static pressure | I = identity tensor | K = viscous stress tensor | F = body force vector field

## Slide 5
Grid Independent Study
120 x 1200 elements ; refined at the wall
Grid Independent Mesh (N = 120)
Baseline Selection: N = 120
Relative change from N = 120 to N = 160 < 0.35%
Grid Independence Study

## Slide 6
Boundary Conditions
Location
Condition
Equation
Vessel wall
(no-slip)
No-slip axial velocity
Radial velocity = Vw / ū₀
Inlet
(x = 0)
Womersley pulsatile velocity
Uniform LDL concentration
Axis of
symmetry
Streamline; zero vorticity
Zero radial conc. gradient
Outlet
(x = 10R₀)
Extrapolation condition
(no upstream reflection)
Wall
(LDL conc.)
Convective flux = diffusive flux
at impervious vessel wall
0

## Slide 7
Results: Steady-State LDL Concentration Profiles
Time-averaged normalised luminal surface LDL concentration (Vw = 4×10⁻⁶ cm/s)
Fig. 2a — Axial distribution (z/R₀)
Fig. 2b — Radial distribution near wall (zoomed)

## Slide 8
Results: Pulsatile Flow — Steady Periodic State (Fig. 3)
Cw/C0 vs phase angle over one cardiac cycle (Vw = 4×10⁻⁸ m/s)
Fig. 3a — D = 5×10⁻¹² m²/s (Sc = 6.6×10⁵)
Fig. 3b — D = 1×10⁻¹¹ m²/s (Sc = 3.3×10⁵)
Fig. 3c — D = 2×10⁻¹¹ m²/s (Sc = 1.6×10⁵)

## Slide 9
Results: Effect of Filtration Rate & Wall Shear Rate on C̄w/C₀
Time-averaged normalised wall LDL concentration vs. Vw and wall shear rate G̅w
Fig. 4a — C̄w/C₀ vs filtration rate Vw (linear increase)
Fig. 4b — C̄w/C₀ vs wall shear rate G̅w (inverse relationship)

## Slide 10
Key Findings
Concentration polarization of LDL is confirmed under both steady-state and pulsatile flow; time-averaged luminal LDL concentration is 5-14% above bulk concentration.
Axial C̄w/C0 increases along the artery, with a steeper rise at higher Schmidt numbers.
Radial C̄w/C0 remains nearly uniform in the core flow but rises sharply near the wall, forming a concentration boundary layer.
Pulsatile flow causes periodic fluctuations in LDL concentration.
C̄w/C0 increases linearly with filtration rate through the vessel wall.
C̄w/C0 decreases inversely with wall shear rate, indicating highest LDL accumulation at low-shear regions.
Pulsatility raises time-averaged surface concentration slightly above the steady-flow value.
Results support regional LDL accumulation as a mechanism for atherosclerosis localization.